## Slide 1: Microcontroller Programming

## Slide 2: Robot Hardware
Two main components to program
  Motors – Give Output
  Sensor Panel – Get Input
Notes: Hv to tell that only these two components are required as inputs and outputs.

## Slide 3: Controlling Motors
Uses Pulse Width Modulation
L298 Driver IC
  Can bear the load current of the motors
  Can control direction of rotation
  Has 3 inputs (for each motor)
    One PWM pin
    Two direction pins
Notes: Shakya explains PWM in previous slides
So have to explain why to use L298

## Slide 4: Sensors
8 IR sensors used
OP-AMP circuit is used to convert analog signal to digital input
Each sensor pin outputs 5V in white background and 0V in black background
Software functions exists to check input state

## Slide 5: First Program – Blinking a LED
Software Used – PIC C
  Easy to use
  Automatic configuration settings
  No need of in-depth knowledge
Creating a new Project with PIC C - Demo

## Slide 6: Blinking a LED - Demo
Steps:
  Apply voltage to a Pin
  Apply a delay
  Remove voltage from Pin
  Apply a delay
  Go to Line 1
Notes: While Doing the presentation first write output high, then output low then explain requirement of delay.
Explain that Goto Line 1 – creates a loop

## Slide 7: Blinking a LED - Demo
Software Functions needed:
Naming – PIC C names pins as PIN_A0, PIN_A1 etc.
Apply Voltage Output - output_high(PIN_NAME);
Remove Voltage - output_low(PIN_NAME);
Apply a delay - delay_ms(Time_In_Milliseconds);
Loop – while(1){ Code_To_Loop}
Notes: Show a datasheet, how to find a pin and its name.

## Slide 8: Blinking a LED - Demo
Actual Code:
while(1){
output_high(PIN_A0);
delay_ms(1000);
output_low(PIN_A0);
delay_ms(1000);
}

## Slide 9: Second Program – Reading Input
Steps:
  Check Status sensor input
  If input is high, light up a LED
  Else, don’t light up the LED
  Go to line 1

## Slide 10: Second Program – Reading Input
Software Functions needed:
All functions from previous example
Read input status - input (PIN_NAME)
  Usage:
    Value = input (PIN_NAME);
    Value is a variable.
    If input is high, value = 1
    If input is low, value = 0

## Slide 11: Second Program – Reading Input
Actual Code:
while(1){
int value;
value = input(PIN_B0);
if ( value == 1) { output_high(PIN_A0); }
else{ output_low(PIN_A0); }
}

## Slide 12: Controlling Motors
Steps:
Setup PWM Configuration – Automatically done by PIC C software
Set motor directions
  One direction pin – high state
  Other direction pin – low state
Set rotation speed (PWM duty cycle)

## Slide 13: Controlling Motors
Our Configuration:
Left Motor: direction pins – RD6, RD7
PWM pin – RC2/CCP1
Right Motor: direction pins – RD5, RD4
PWM pin – RC1/CCP2
Notes: Have to explain direction pins are normal I/O pins and PWM pins are special pins connected to PWM module. So PWM pin needs to be controlled by special functions.

## Slide 14: Controlling Motors
Demo – setting PWM configuration
Software functions
  set_pwm1_duty(value) – speed for left motor
  set_pwm2_duty(value) - speed for right motor
Value is a integer variable between 0 and 1023. speed changes according to this value.

## Slide 15: Controlling Motors
Actual code for left motor:
output_high(PIN_D6);
output_low(PIN_D7);
set_pwm1_duty(100);
while(1);
Notes: Explain while(1)